## Slide 1: Unrolling algorithms for tomography of limited angles
Group component:
Kamal Nishantha Angunna Gamage
Matteo Fontana
Giuseppe Spathis
Supervisor:
Elena Loli Piccolomini

## Slide 2: Project description
Goal: Reconstruct CT images from limited-angle sinograms using an unrolling method (Adler et al.) with a Residual U-Net architecture.
Comparison: Evaluate the unrolling Plug-and-Play algorithm against a Total Variation (TV) model-based reconstruction and Filtered Back Projection (FBP).

## Slide 3: Theory Introduction

## Slide 4: Problem description

## Slide 5: Methodology
We have compared 3 algorithms:
Filtered Back Projection.
Total Variation regularization.
The unrolled method: Learned-Primal dual.

## Slide 6: FBP - Theory
FBP (Filtered Back Projection) is a direct method for image reconstruction from sinograms (Radon projections).
Rθ​(r) is the Radon transform (i.e., projection at angle θ)
F and F−1 are the Fourier and inverse Fourier transforms
∣ω∣ is the ramp filter in the frequency domain (or other filters like Shepp–Logan, Hamming, etc.)
This formula:
  Filters the sinogram in frequency domain (amplifying high-frequency components).
  Back-projects the filtered projections over the image domain.
Fast and non-iterative, but sensitive to noise and artifacts.

## Slide 7: FBP - Implementation
Function used: skimage.transform.iradon
Input: sinogram
Main parameters:
  theta = geometries
  filter_name = "ramp" (Ram-Lak filter)
Output: reconstructed image using inverse Radon transform.

## Slide 8: TV - Theory
Enhance image reconstruction by preserving edges while removing noise.
Total Variation is defined as:
Solves problems of the form:

## Slide 9: TV - Implementation
Optimization Algorithm: ISTA (Iterative Shrinkage-Thresholding Algorithm)
Number of Iterations: 1000
Step Size (Learning Rate): 0.005
Regularization Weight(lambda_tv): 0.05 (tuned for balance between data fidelity and smoothness)
Proximal Operator: Chambolle-Pock
Initial reconstruction: np.zeroes_like(img_size)

## Slide 10: TV - Code

## Slide 11: LPD - Theory
Primal Space contains the reconstructed image
Dual space contains the sinogram
In our case, we use 10 unrolled iterations, and for each iteration we have two U-Nets:
- a primal U-Net, designed to denoise the image
- a dual U-Net, responsible for correcting the reconstruction to ensure fidelity to the sinogram.

## Slide 12: LPD - Implementation
Hyperparameters:
- Learning rate: 10^-3
- Number of unrolled iteration: 10
- Epochs: 20-30
Batch size: 4

## Slide 13: LPD DESIGN
Each U-Net consists of two layers, with 32 features in the first and 64 in the second, and includes residual blocks between them.
Total params: 7,555,860
Trainable params: 7,555,860
Non-trainable params: 0

## Slide 14: Introducing the experiments
Test Geometries:
  30 angles in [-30°, 30°]
  30 angles in [-15°, 15°]
  30 angles in [0°, 180°]
  Each tested with and without noise (noise level = 0.1)
Metrics:
  Relative Error (RE)
  PSNR
  SSIM
Outputs:
  Reconstruction results for a selected image, with zoom-in area visualizations
  Average metrics across a subset of the test set, presented in a .xlsx file

## Slide 15: Mayo dataset
Provided by the private U.S. institution Mayo Clinic through the Cancer Data Access System (CDAS) of the National Cancer Institute.
It contains 3,305 anonymized grayscale CT images (512×512 px) of human lungs from 10 patients.
Dataset: Mayo Clinic CT Dataset

## Slide 16
Geom (-15°, 15°)
Noise = False

## Slide 17
Geom (-15°, 15°)
Noise = True

## Slide 18
Geom (-30°, 30°)
Noise = False

## Slide 19
Geom (-30°, 30°)
Noise = True

## Slide 20
Geom (0°, 180°)
Noise = False

## Slide 21
Geom (0°, 180°)
Noise = True

## Slide 22: Results on a subset of the test set

## Slide 23: Conclusions
TV regularization:
Sometimes achieved higher SSIM in small regions with respect to LPD → better local detail
In 0°–180° geometry, surprisingly competed closely with LPD
Outperformed LPD in all other metrics, except SSIM on single image
The slowest method
Less sensitive to noise than FBP
The regularization parameter λ needs to be carefully tuned
FBP:
Worst performance overall
Very sensitive to noise
The fastest method
LPD:
Best performer for ±15°, ±30° geometries
Robust to high noise levels
Outperforms TV on noisy images in the 0°–180° range when analyzing a subset of the test set
May need longer training to fully exploit wide angular ranges (e.g., 0°–180°)

## Slide 24: Bibliography
J. Adler and O. Öktem, "Learned Primal-Dual Reconstruction," in IEEE Transactions on Medical Imaging, vol. 37, no. 6, pp. 1322-1332, June 2018, doi: 10.1109/TMI.2018.2799231.

## Slide 25: Thank you for your attention!